## Slide 1
Information
On
LN2 & cryocan
Dr. Vikas Sachan
Veterinary Gyn and Obst

## Slide 2
Liquid Nitrogen (LN2)
- AI center
- container for LN2 for storage (52/55 liter)
- frozen semen straws storage cryocan (35 litre)
- Small portable LN2 container (3-5 litre)

## Slide 3
Liquid nitrogen
- BP -1960C and FP -2120C
- In special container : LN2 cylinder or cryocan
- Double-walled metal/aluminium vacuum vessel
- Efficient insulation system
- Inner chamber, outer chamber and a bad heat
conductor non-metallic neck
- A high quality insulator material (No heat
exchange) with maintained vacuum system
: Between inner and outer chamber

## Slide 5
Failure of vacuum system
- Loss of the gas
Frost line (top of container) - increased evaporation
(due to damaged container)
Neck tube - delicate part
(hold weight of inner chamber)

## Slide 6
LN2 cylinder
-Kept on rubber, jute or wooden carpet
- No Wet floor, hard cement or chemicals
- corrosion - Loss of vacuum system
- Always in vertical position
- Never be tilted or rolled to avoid any damage
- No piling one cylinder above other

## Slide 7
LN2 cylinder
- Shifting with platform base trolley
- Place in cool place with no direct sunlight
- LN2 holding capacity : reduced

## Slide 8
- Arrangement of extra cryocan
(in case of appearance of frost line)
Careful handling to avoid damage to vacuum knob
No jerk or shock/vibration during lifting/carrying
- Damage to the neck tube: loss of vacuum system
No Punching or drilling on the container wall

## Slide 9
LN2 cylinder - Secured with rubber band rings
(As shock absorbent)
- Careful while transporting filled cryocans in bus or train
(sudden evaporation : Panic situation)

## Slide 10
Neck : dry with cloth or tissue paper time to time
(to avoid jamming of the neck plug)
Lid should : vertical position
Lids or canisters : never be exchanged
(damage due to tight fitting)
(frost formation due to loose fitting)

## Slide 11
No Frequent opening, closing or shifting
: to keep evaporation rate minimum.
Charging and filling : Slowly
Non-splashing manner
Use funnel
Avoid overfilling of gas.

## Slide 12
Metal or wooden dipstick :measure the LN2 level
(No Plastic or any hollow rod)

## Slide 13
Filling new container : Wait for 24 hr for charging
Refilled to its full capacity
Frost appearance on first filling
(Vanishes by its own within one or two hours)
First noting of the LN2 level : After 10 days
(Normal time taken for thermal balance by the new
container)

## Slide 14
- Use of protective clothing and eye glasses
- To avoid any direct contact of the LN2
- LN2 : Non-toxic and Non-inflammable gas
- But direct contact : tissue damage (frost bite)
- Water should be used immediately
- Poorly ventilated room : Suffocation

## Slide 15
- Frozen semen doses - in a well-ventilated room
(all weather safe storage area)
Identification marking and mapping of semen storage
Frozen semen : No exposure above liquid nitrogen
(thermal shock)
Canister : Not exposed over and above the neck
Transferring the semen straws : Use thermocole box
(Fast transferring : 5 seconds exposure of straw in air)
Maintain proper level of liquid nitrogen
Details of semen dose and AI centre
: Updated after every supply

## Slide 16
- LN2 level below the canister
- Lost cold chain
- whole of the semen stored spoiled
- Discard all the semen doses
- Replenish the LN2
At the time of AI , Semen straw
- No exposure above LN2 : more than 10 seconds

## Slide 18
- AI kit - Scissors, Thermometer/thaw monitor, Thawing Tray, Forceps, Sheaths with sheath container, AI Gun with container, Plastic gloves, Lubricant, Isopropyl alcohol/ surgical spirit, Tissue papers, Clean towel, Thermos-flask with hot water, apron, Tags, pins and tag applicator etc.
Stainless steel AI guns and AI sheath
: Approved by BIS (Bureau of Indian Standard)

## Slide 19
- Clean AI gun, scissors and other accessories
: When soiled
: Once a week with hot water and air dry
- Sanitize the AI gun and the scissor
: With Isopropyl alcohol after every insemination
- Surgical spirit and soaps : lethal to semen
- Aprons, towel etc : washed properly
- Cold fumigation in formaldehyde chambers (AI box)